BBLR MD 24 July 2007

Present: Jorg, Ulrich, Gerard, Rogelio, Guido, Andrea, Jena-Pierre

8:15 Gerard will set BBLR to -20 mm from the beam

8:27 Fast BCT launched; data saved to /user/slops/data/2007/MD-DATA/BBLR-24jul07/BCT

Multi-Q data saved to /usr/slops/data/2007/OP-DATA/multiQ/

MD1 beam, Intensity ~10^11 protons, single bunch

About 5-10% intensity loss on the ramp

Initial Tunes 0.135, 0.18

8:40 Gerard confirms that BBLR2 has been set

Plan to go to approximate LHC tunes 0.31, 0.30 (not 0.32 since lifetime is too bad close to 1/3 resonance)

Loss data saved to /user/slops/data/2007/MD-DATA/SPS_BBLR-24jul07/BLM

Total rf voltage was trimmed in last days, less than 1 MV capture voltage; reset settings; less captures losses and less losses on ramp

Excite BBLR1 from 11200, to 12700 ms (length of flat bottom 1500 ms)

BBLR1 at -120 A

Tune shift -0.006 for +120 A in BBLR1 indicates distance 14.8 mm

Go to lhc tunes QH=0.311, QV=

Excite BBLR1, tune change 0.002 indicates distance 25.6 mm, but there is evidence of coupling, which could have obscured this measurement

12x1.439 microrad kick  -> 18.8 mm distance

BBLR2 +120 A, DeltaQH+0.004, DeltaQV-0.002

Similar 12.7x1.439 microrad -> 17.8 mm

DeltaQV->24 mm, DeltaQH->18.7 mm

Change QV to 0.28, QH 0.31

Separate tunes, BBLR2+120 A gives DeltaQ+0.004, DeltaQV-0.004

Tune shifts -> distance ~ 17.0 (V) and 18.7 mm (X)

Kick interpretation takes into account factor

Sin(pi Q)/Sin(pi Q0)~1.439 in response matrix

Now coupling correction by Rogelio

Minimize coupling line / main line ratio by adjusting skew quad for tunes QH=0.31, QV=0.30

Wire scans ongoing by Rama, Elena et al

10:55 done. Decoupling -0.0004, final ratio 20/220.

Dampers off.

Wire scan result, BWSH51995

GammaEmitX=1.8 micron, GammaEmitY=1.5 micron

EmitX=64.4 nm. EmitY=53.6 nm

Betax=83.5 m (99 m?), betay=27.3 m (22 m?)

If GammaEmit=1.5 micron,

Need Iwire=107 A, and distance=13.5 mm

If GammaEmit=1.8 micron,

Need Iwire=128 A, and distance=14.8 mm

Wire scanner at 51631 now, which changed the beta functions (see the values in parentheses above)

Chromaticity measurement and correction by Rogelio and Rama.

Before correction QH’~1, QV’~5;

Deltap/p=+2e-3 (beam is lost for negative offsets).

After correction Q’ ~ 1-2  in both planes.

Move beam closer to the wire by 4 mm, which should provide a distance of about 14 mm, roughly equivalent to 9.5 sigma.

Orbit bump -4 mm.

Both BBLRs at 0

0 A,  52913

BBLR1

-30 A, 52952

-60 A, 52985, orbit kick 4.9 (x1.4) microrad indicates 23 mm distance,

tune change too small to be resolved?!

PS down, when back up, the orbit was different.

To check movement direction, higher power: 200A excitation

Moved tune kick to the end of the 26GeV plateau

14:00 beam back

0 A, 53385

16.5 microrad x 1.4 -> 22.7 mm,

DeltaQV=8e-3, DeltaQH=6e-3, -> 16.6 mm, 18.5 mm

Change polarity of wires to have positive excitation

Sigma on wire scanner about 2.0mm, 1.1 mm

GammaEmitX=1.1 micron

GammaEmitY=1.5 micron

(big tails in the vertical profile sometimes give flaky results)

DeltaQH/V=0.005, but tunes too close to conclude

Further separate the tunes to QH=0.31, QV=0.28

BBLR1 +200 A, DeltaQV=+0.007, DeltaQH=-0.004

-> distances 17.7 mm, 22.6 mm

SC 53484 (+/-)

Too much, unclear, move another mm down (should be 10mm from beam)

-200A

Wire off: 0.3122/0.2812

With wire: 0.3125/0.2793

SC 53539

-200 A

We think the orbit ump has the wrong sign

+8 mm

Wire ON: 0.3154/0.2773

+4 mm (wire should be 22 mm - or 14 mm!? - from the beam)

Wire off: 0.3105, 0.2832,  SC 53631

Wire on: 0.3184, 0.2744, SC 53625, 26, 28, 29

-> 16.1 mm, 15.8 mm

another +2 mm

Wire on: 0.3213, 0.2734, SC 53651

Wire off: assume same as before

-> 13.8 mm, 15.0 m

0.3232, 0.2705?

0.3213, 0.2734 Wire on

0.3105, .2842 Wire off

-> 13.8 mm, 14.3 mm

SC 53716

BBLR2 powered, almost no tune shift; so BBLR2 is below the beam

BBLR1 distance 14 mm from beam; BBLR1 wire current scan, BBLR2 off , no tune correction

0 A starting SC 53735, QH=0.3096, QV=0.2861, QH=0.3096, QV=0.2871, intensities 1041 -> 1009, 970->939

200 A starting SC 53752, 0.3203, 0.2783, intensities 934->692, 907->670 (corrected tune->0.31)

100 A starting SC 53761, 0.3135, 0.2842, intensities, 860->765, 1025->903

From SC 53771 on unknown BBLR state

270 A starting SC 53774, 0.3232, QV=?

Tune correction from 53779

Period without beam

SC 53852, H tune corrected QH=.3066, 797->520, 754->518, 769->528

We always kicked at 1440 (at beginning one was 1480 ms).

Now go to 37 GeV.

-200 A, distance still 4 mm, SC 53934

move 3 mm closer to beam

Rogelio takes wire profiles at 2800 (end of ramp 2500 ms) and 4000 ms in the cycle

Kick at 4150 ms

Beam-wire distance still at 14 mm

Sigmay=1.2 mm at 37 GeV

SC 53962 (and earlier), 200 A current,

SC 53964 wire off, sigmaY=1.2 mm

Wire off tune, 0.3077, 0.3154, SC53970

Rebooting some server for tune measurement

SC53991, 0.3074, 0.32422?,  wire off

0.3076, 0.2891, wire off

Large kick for Rogelio SC 54044

Beam +3 mm closer (should be 11 mm), from SC54008

0 A, SC 54010, QH=3074, QV=2901

100 A, SC 54019, QH=3126, QV=2843 ,  -> 12.2 mm, 11.6 mm

200 A, SC 54029, QH=3182, QV=2784, 812 -> 801

270 A, SC 54035, 876->837, 874->836

Another +3 mm closer to ~9 mm distance? (different bump, since correctors are at maximum)

+10 mm with initial bump, outer bump +2 mm

270 A, SC 54060, 649->357, QH=0.33, QH=0.336, QV=0.265;

correct tune SC54074 -> QH=0.3175 , QV=0.2655, 696->403, 590->329

from SC54082, 0 A, QH=0.2833, QV=0.2920 -> 8.7, 8.9 mm, 0 loss

unperturbed tune (take out tune correct) 0.3067, 0.2929

150 A, from SC 54097, QH=0.3220, QV=0.2774 (w/o correction),

607->589, 492->483

180 A, SC 54107, 0.3214, 0.2774 (uncompensated), 767-> 736, 505->472

220 A, SC 54125, intensities 651->536, 528->436, 729->520,

QH=0.329, QV=0.270

250 A, SC 54153, 517->323, 634->397, 516->312

SigmaY = 0.79 mm (0.8 micron Y normalized) -> 0.60 mm

100 A SC 54172, 753->749, 637->631, 753->749

QH=0.315, QV=0.281

150 A, ~9 mm distance, chromaticity scan

assume initial setting is close to 0

Q’~1, 556->544, 480->465, 627->618

Change QH’ by 1.3, SC54205, QH=0.3203, QV=0.2764

QH’-> 3.6, SC54214, QV=2764

QH’->6.2, SC54223

QH’->8.8, SC54230

Rf voltage 2.6 MV at 37 GeV

QH’->11.4, SC54242

Wire off SC, QV’~11.4, 54247

Wire on SC 54252

QH’->14, SC 54256

QH’->16.6, SC54262

Back to original QH’ setting, SC54269, QH=0.31213, QV=0.2764

QV’->3.6, SC 54277

SC54283, QV’=6.2

SC54290, QV’=8.8

SC54298, QV’=11.4

SC54309, QV’=14

Chromaticity back

SC 54343, BBLR off, 0.3066, 0.2910

BBLR1 200 A, distance scan

SC 54349

-2 mm out (11 mm from wire center), from SC ~54349, intensities 755->738, 783->761, 736->721 (should be 11 mm from wire)

-4 mm out (13 mm) – “8”, from SC 54361, intensities, 847->843, 814->811, 903->900

0 mm (9 mm), SC 54370, intensities, 607->571, 605->560, 662->587

QH=0.3271, QV=0.

Save wire scan, 0.86 (start of 37 GeV), .92 mm (1300 ms after start of 37 GeV) sigmaY, 637->594, 468->419, 546->506

+1 mm (8 mm from wire center), SC54395, 549->311, 451->281,

408->267 [all without tune compensation, tune measurement does not work anymore]

Check with multiQ if kick is visible, QH=0.329

Correct tune to QH=0.31 SC 54409, 425->270, 345->262, 484->305, QH=0.3106, QV=0.2783 (tune corrected)

SC 54422 multi-Q has interesting lines

Another +1 mm (7 mm from wire center) SC54427, 461->208, 358->149, 300->123

Current to 150 A, tune correction left implemented

7 mm from wire center, SC 54437, 368->271, 465->297

Current to 120 A

7 mm from wire center, SC 54442, 388->358, 431->386, 413->385

QH=0.3057, QV=0.2769

Current back to 150 A, SC 54450

7 mm from wire center, SC 54450, 287->231, 286->235, 453->300, 447->293, QH=0.3096

8 mm from wire center, SC 54462, 485->465, 413->390,  492->468

Again to 7 mm SC 54466, 370->266, 424->302, 389->269

QV=0.2743, QH=0.3105

Another + 1 mm, 6 mm from center, SC 54476, 281->116, 333->145, 309->141

QH=.319, QV=0.2618

Lower wire current to see where effect disappears

100 A SC 54491, 358->318, 240->226, 250->236

80 A SC 54497, 217->215, 210->203, 236->228

50 A SC 54501, 225->224, 230->227, 238->237

QH=0.2959, QV= 0.2854

30 A SC 54507, 342->342, 311->310, 230->230

QH=0.2930, QV=0.2882 at 30 A

SC 54520 BBLR off

Tunes w/o wire QH=2871, QV=0.2968/.2956

-> 6 mm (X), 5.2 mm (Y)