BBLR MD 29.07.2004

G. Burtin, J.-P. Koutchouk, Y. Papaphilippou,  F. Roncarolo, T. Sen, V. Shiltsev,

J. Wenninger, F. Zimmermann

9:30   BBLR moved to 19 mm from the beam

9:40   12 bunches, 9.6e11 total intensity

PS lowers total intensity to 3.5e11

notice different current shape for the two BBLRs, partly corrected by changing the

current ramp profile, BBLR2 has 0.7A overshoot at 240 A;

If both BBLRs currents are positive the compensation is active (opposite to the

expected polarity)

orbit is logged continuously; three wire scanners (2 rotational and 1 linear) can be

operated in the same cycle

data are saved to special MD directory (name …”BBLR04”)

c223   tunes 0.1755, 0.1538 knob setting xix=0.2, xiv=0.03 (about Q’~1 in both planes)

radial octupole -0.875, vertical octupole 0

emittance 2.5 normalized, all BBLRs off

increase emittance to 4.0 by mismatch in injection line

ramp up BBLR from 100 to 1000 ms after injection, down ramp from 4000 ms.

c.306  11:36 scan on  1st BBLR, 240 A

c. ~354 both BBLRs on

c.365   BBLR2=270 A

c. 368  BBLR2=210 A

c. 376  BBLR2=180 A

c.386   240 A BBLR1 only, BBLR2 off

by the way all dampers are off during this MD

wire scans at 400, 1100, 2000, 3900 ms

tune measurement, DeltaQV shifts by about 0.004 due to the BBLR

optimum compensation current is about 210 A

suspect that BBLR2 is 1.5 mm too close to the beam

wire scans also at 1300 and 1500 ms indicate that most of the emittance shrinkage

occurs between 1100 and 1300 ms

c.523   both BBLR at same current

c.525 tune measurement

tune shifts look slightly overcompensated (~1e-3)

12:40   take 1000 turn data with kicks at different amplitudes

1 BBLR, 2 BBLRs, showing that coupling is due to the wire

wire scans

lifetime slightly better (no obvious reason)

BA5 amperemeter indicates BBLR2 15 A weaker (opposite to experimental

indication)

c.580   wire scans, tune measurement

c.626   BBLR2 +1 mm (20 mm)

c.664   BBLR2 +2 mm (21 mm)

emittance suddenlu changed from 6 to 2.5

reason unclear (PS does not know either)

13:28  increase mismatch to enhance emittance

c.760  BBLR2 +3 mm (22 mm)

c.780  BBLR2 +4 mm (23 mm)

c.792  BBLR2 +5 mm (24 mm)

c.813  BBLR2 +1 mm (20 mm) – leave it here for the rest of the MD

c.826 BBLR2 270 A 14:02

c.841 210 A

c 859 180 A

c.871 150 A

c.881 120 A

c.891  90 A

c.900  60 A

c.911  30 A

c.925   0 A

c.931  both BBLRs at 0, wire scans, 1000 turns

orbit is measured at 1500 ms

c.958 BBLR1 0, BBLR2 240 A

c.976 240 A, 240 A

c.986 0 A, -240 A

c.1000 -240 A, -240 A

wire scans, 1000 turns

14:54 QH up in 0.002 steps

c.1040? +0.002 (.1761,1529)

c.1050  +0.004

c.1059  +0.006

c.1065  +0.008

c.1073  +0.01

c.1088   0, 0

c.1097 -0.002

c.1103 -0.004

c.1115 -0.006

c.1124 -0.008

c.1137 -0.01   0.165, 0.153

c.1172  no BBLR

two wires reduce lifetime by factor 2 compared to case w/o BBLR

c.1205 -240 A, -240 A, +0.002 QV

c.1213 +0.004

c.1220 +0.006

c.1224 +0.008

c.1228 +0.01

c.1248 0

c.1255 +0.002

c.1257 -0.004

c.1262 -0.006

c.1272 -0.008

c1276  -0.01, 0.1643, 0.1453

16:12 scan emittance, wire scans

c1328 turn off BBLRs at optimum working point (last)

16:23 lower emittance

16:31 -240,-240

16:34 -240, 0

c.1453 -240,-240

c.1512 both BBLRs 0, 0

1000 turns

c.1558 LHC tune, 0.307, 0.319 BBLR 0,0 DeltaN-37,17,100,17

c.1590  -240, 0, DeltaN=118, 143, 55

c.1601  -240, -240, DeltaN= 22, 35, 20, 34

c.1661  nice cycle, larger emittance, DeltaN=71,69,46

18:00 48 bunches from now (PS 40-MHz rf problems)

18:15 attempt to move H scraper (was in correct cycle)

plan for Friday: V tune scan at LHC tune

QV=0.27-0.32

QH=0.31 constant

With both BBLR, one BBLR, and none

Other issues:

Scraper functionality

Emittance vs, time w/o BBLR

Scan lifetime vs. emittance with & w/o compensation

Tune scan with 1 BBLR (tune sensitivity)

BBLR MD 30.07.2004

F. Roncarolo, T. Sen, J. Wenninger, F. Zimmermann

Y tune scan around LHC working point with BBLR off, both BBLRs and only 1 BBLR

11:53 set up LHC like tunes

tune measurement kicks at 1500 and 1520 ms

12:05 blow up emittance by mismatch to a value of ~4-4.2

tunes 0.309, 0.3188

both BBLRs off

c5630 tunes .309, .3188

N0 (at 1000 ms)=3124, Nfinal (at 3440 ms)=3056, DeltaN=68

3669, 3570, 99

3554, 3456, 98

3017, 2942, 75

c5646 QV +0.005 -> 0.324

2379, 2157, 222

2979, 2813, 166

2598, 2389, 209

c5655 0.314

3226, 3185, 41

3810, 3746, 64

3307, 3266, 41

c5665   0.309

4051, 4007, 44

3291, 3193, 26

3455, 3414, 41

3170, 3132, 38

c5673   0.304

3869, 3817, 52

3341, 3249, 92

3962, 3913, 49

3589, 3541, 48

c5685    0.299

2155, 2075, 80

3334, 3294, 40

4059, 4009, 50

c5693   0.294 (measured 0.289 and 0.292, perhaps Qs sideband)

3416, 3337, 79

3593, 3514, 79

3790, 3701, 89

c5704   0.289 (measured 0.289)

3340, 3299, 41

3605, 3568, 37

3769, 3729, 40

c5711   0.284

3794, 3758, 36

3852, 3813, 39

4030, 3982, 48

c5720 0.279

3445, 3408, 37

3722, 3681, 41

3733, 3695, 38

c5728 0.274

3570, 3530, 40

3751, 3713, 38

4587, 4531, 56

c5737 0.269

3831, 3745, 86

3290, 3215, 75

3675, 3632, 43

measured tunes 0.312, 0.269

emittance measurement BBLRs still off

turn on both BBLRs at -240 A

repeat emittance measurement

13:14 finished wire scans

c5801 BBLR -240 A, -240 A tunes at 0.312, 0.267

corrected to 0.312, 0.269

4000, 3897, 103

4318,4189,129

3476,3356,120

3676,3577,99

c5840 0.274 setting (0.272 meas.)

3798,3711,87

3709,3579,130

3766,3675,91

c5855 0.279 (0.277 meas)

3946,3770,176

3916,3744,172

c5862  0.279 (corrected)

3710, 3578, 132

3177,3092,85

3208,3108,100

c5871  0.284 (QH 0.3112)

3480,3385,95

3499,3445,54

3170,3123,47

3817,3748,69

3303,3246,57

c5883  0.289

3142, 3062, 80

3579,3531,48

3514,3466,48

4238,4185,53

c5894  0.294

3248, 3200, 48

3987, 3938, 49

3919, 3872, 47

c5900  0.299

3337, 3247, 90

3163, 3109, 54

3390, 3354, 36

3377, 3336, 41

3168, 3123, 45

c5912  0.304

3138, 3104, 34

3111, 3075, 36

3430, 3382, 48

c5918  0.309

3068,3026,42

3139,3103,36

3331,3297,34

c5925  0.314

3136,3033,103

2922,2866,56

2948,2891,57

3204,3139,65

c5934  0.319

2651,2535,116

3264,3106,158

2840,2712,128

c5945  0.324

2328,2076,252

2483,2226,257

2175,1834,351

c.5955  0.319 wire scans (still -240 A, -240 A)

c.5982 1 BBLR tune shift compensation

c5988 0.3083, 0.3189

c5992 0.3110, 0.3187 – leave it likes this

2841, 2608,233

2921,2688,243

3302,3048,254

2899,2641,258

c6022 0.324

2410,2140,270

2524,2263,261

2563,2284,279

c6030  0.314

3127,2865,262

3107,2954,253

3087,2836,223

c6037  0.309 (not measured – difficult due to coupling)

3782,3445,337

4135,3834,301

3295,3058,237

c6045  0.304 (meas.0.300)

3266,3017,249

3167,2972,195

3418,3198,220

c6052  0.299 (meas 0.294!, QH 0.315)

3344,3210,234

3891,3686,205

3375,3247,128

3298,3150,148

c6066  0.290 (meas.)

3534,3429,105

3425,3318,107

3646,3522,124

3486,3371,115

c6074   0.285

3957,3779,178

3565,3446,119

3737,3614,123

c6080   0.280

3831,3700,131

3366,3179,187

3694,3515,179

c6087   0.275

3938,3527,409

3859,3480,379

3476,3136,340

3889,3551,338

c6096   0.270 (meas.)

4122,3870,252

3681,3440,241

3925,3669,256

3289,3073,216

14:40 back to LHC tune

current scan 2nd BBLR

1st BBLR at -24 0A

tunes 0.31, 0.32 (LHC)

c6115 -240,-240  3121,3011,110

c6120 -240, -270

3225,3112,113

3949,3829,120

3983,3848,135

c6131 -240,-210

2005,2847,158

3734,3540,194

3339,3229,110

3698,3582,116

3599,3491,108

c6144  -240, -170

2707,2586,123

c6149  3445,3295,150

3270,3107,163

3426,3304,122

3574,3443,131

3530,3403,127

c6180   -240, 0 adjust tunes

c6187   -240, 0

-240, 0  (0.308, 0.320)

3480, 3221, 259

2983,2756,227

3531,3282,149

2914,2702,212