Switch & recabling of BBLRs

Upstairs:

Push red emergency button on power converter

Open safety box, lock it with cadena

We will use old converter for the study with common supply

Tunnel:

Remove protection cover

Close water

Re-connect power cables (e.g., disconnect old ones)

Flowmeter indicator needs to be white when water is switched back on

(very sensitive), can be reset with screw driver from underneath

If there is a debit fault from the flow switch,  ‘external chain’ error will light up on the power supply

Upstairs:

To reset power converter, push boxes back in, and turn handle,

pull out emergency button, and push ‘reset’ on converter

Position control of  the BBLR

1 mm = 400 steps

Motor 1: 19 mm – 0921 on resolver

22 mm – 1230 on resolver

Motor 2: 19 mm – 2617 on resolver

22 mm – 2923 on resolver

plus sign moves wire away from beam

“half step” should be selected

push start to active motion

help from Jean-Luc Pasquet