BBLR MD 27 August 2007

Present: Jorg, Ulrich, Guido, Jean-Pierre, Rama, Frank

20:00 reset flow switch with help of Jean-Luc Pasquet, Christophe Vuitton, Angelito Herve

Single bunch 5e10 ppb

Chromaticity 0.05 in both planes

Bunch length (4 sigma) = 4 ns

4 MV at 55 GeV

21:20 emittances at 55 GeV/c (SC 51317): 1.7 micron (horizontal), 1.9 micron (vertical)

Orbit corrected <0.5 mm in y, -1.9 mm offset in x

Chromaticity low

Tune kicks 18400 and 18450, 1 kV

21:41 tunes: Qx=0.3070, Qy=0.2783

21:47 orbit bump, SC 44393

SC 44731: start BCT and fast BCT

Save data to /user/slops/data/2007/MD_DATA/ SPS_BBLR_27_Aug07

+ 9 mm (from orbit center)

SC 44405

26 GeV/c from 0 to 10860 ms

55 GeV/c from 12760 to 18760 ms

BBLR 50 A: 13000 ms up, 18500 ms down

23:09 SC44550, 0.3096, 0.2764

SC 44554 100 A, no clear tune change

SC 44555 200 A

SC 44557&58 270 A, 0.3145, 0.2686?

sc 44560, 0.3174, 0.2676

-> estimated distance 12.9 mm, 12.6 mm

(10.8 mm was expected from bump and BPM readings)

smoothen ramp of wire

kick angle: 27 microrad -> 12.8 mm distance

all distances consistent with 9.9 sigma_y separation

SC 44579 set wire current to zero

-> no funny step changes in current anymore

increase x chromaticity + 0.01 Q’x,y

23:27 SC44585

-> steps again

SC 44610

kicking since some time at 12400 and 12400 ms

smoothened BBLR ramp pattern

45 A current

23:44 SC 44617, 13250 ms start of BBLR ramp

Kicking again at 18400 ms

SC 44622

270 A excitation, Q=0.3174, 0.2681

0.3174, 0.2671; 0.3169, 0.2681

increase y chromaticity +0.02 to check

23:52 SC 44635

chromaticity was set back – check when!?

23:59 SC 44645

Go 3 mm closer to wire

18400, 18450 ms

0.3155, 0.2598

Move down ramp earlier

tune shift 0.3262, 0 .2598, wire at 270 A

-> inferred distance 8.3, 8.8 mm

-> about 6.6 sigma_y separation

Tune correction SC 44658 ~0.3071, 0.2754

180 A SC 44668, 0.3003, 0.2832

SC 44674, correct tune 0.3071, 0.2837

100 A SC 44680, 0.3008, 0.2852

orbit moves 1.5 closer to the beam at 270 A excitation

beam unstable in both planes when losses occur

SC 22688

0:27 SC 44699

increase Q’ y 0.01 units (~2.5 units)

0:35

SC 44720

move beam closer to wire

expect to be at 4.5 sigma from wire center (5.5 mm)

SC 44727

increase Q’x 0.01 units

still step losses

tune signal almost disappeared

SC 44733

octupoles

0:49

SC 44740

move out 2.5 mm

no step losses anymore

0:51

SC 44746

50 A

negligible losses (even with higher chromaticity)

0:55

SC 44753

150 A

chromaticity scan

reset to 0 (0.05) chromaticity in both planes

change qy’ +0.01

SC 44767, 1:02

Total Qy’ +0.02 SC 44770 (or Qx’?)

+0.03 1:05 44773

+0.05 1:06 SC 44776

+0.07 1:07 SC 44778

1:09 SC 44781

200 A

1:11 SC 44785

+0.12 Qx’

1:15, SC 44792

+0.22 Qx’

1:19, SC 44800

+0.1

1:20, SC 44802, +0.3

1:22, SC 44806, +0.4

1:24 large x kick, 0.1792, 12600 ms

14600 ms, Qx=0.3164

1:25, SC44814, Qy’=0.5

1:28, SC 44820, Qy’=0.7

1:30, SC44823, Qy’=0.9

1:32, SC 44825, Qy’=1.1

1.34, SC44829, Qy’=1.3

1:35, SC44832, Qy’=1.3, 150 A

1:36, SC 44824, Qy’=1.3, 100 A

1:38, SC 44836, Qy’=1.3, 50 A

1:40, SC 44840, Qy’=1.3, 0 A