BBLR Machine Development

September 9th 2004

Preparation:

Trouble with BBLR control, probably due to a confusion between control boxes

Preparation:

13:15: Beam on

Set-up data: 	Intensity of 1012 , i.e. 9 x 1011 per bunch

Orbit rms (1.6, 1) [mm], -0.3mm @ BBLR

Tunes (0.311,0.302)

Chromaticity 26x(0.05,0.1)

1000-turn tests: Kicks of 2mm in both directions

13:40: BPM timing seems to be problematic.

BPM delays adjusted (cycles 176631 to 176712)

14:02: Final delay values for each BPM group: 28.1,14.2,3.3,21.4,17.4,18 [μs]

14:30: Coupling seems to be significant, an empirical minimization is applied. It looks much better in the 1000-turn data.

14:40: PS down

17:15: PS Back

Emittance: Timing 20, 3000, expert program gives noise, using standard application

Cycle		εn

? 	   (2.13 / 1.91) 10-6   	  (ws 519)

177504   (2.165 / 2.157) [mm] (ws 414)

177524   (2.19 / 1.84) 10-6 	  (ws 519)

177528   (1.70 / 1.60) 10-6  (injection oscillation corrected)

177532   (1.76 / 1.61) 10-6

177536   (1.74 / 1.53) 10-6

177540   (1.71 / 1.62) 10-6

Timing:

BBLR :	From 500 to 0 and from 4300 to 5200

Kicker  :   	3500

Emittance:	20, 3220

Rescaling:

ε = 1.72 x 10-6

Iw = 122.5 A

dw = 14.5mm to center

Bump = -5.75 mm

cycle 177606, εx =1.95 x 10-6

Experimental Procedure

| NO BBLR |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Cycle # | Qy | Qx |  |  |  |  |  |
| 177787 | 0.3 | 0.31 |  |  |  |  |  |
| 177794 | 0.295 | 0.31 |  |  |  |  |  |
| 177803 | 0.29 | 0.31 |  |  |  |  |  |
| 177811 | 0.284 | 0.31 |  |  |  |  |  |
| 177819 | 0.279 | 0.31 |  |  |  |  |  |
| 177827 | 0.274 | 0.31 |  |  |  |  |  |
| 177840 | 0.304 | 0.31 |  |  |  |  |  |
| 177849 | 0.31 | 0.31 |  |  |  |  |  |
| 177859 | 0.314 | 0.31 |  |  |  |  |  |
| 177871 | 0.32 | 0.31 |  |  |  |  |  |
| 177879 | 0.325 | 0.31 |  |  |  |  |  |
| BBLR1 @ 122.5A |  |  |  |  |  |  |
| 177890 | 0.30 | 0.305 |  |  |  |  |  |
| NO BBLR |  |  |  |  |  |  |
| 177902 | 0.3 | 0.31 |  |  |  |  |  |
| BBLR1 @ 122.5A |  |  |  |  |  |  |
| 177916 | 0.305 | 0.305 |  |  |  |  |  |
| 177919 | 0.305 | 0.31 |  |  |  |  |  |
| 177943 | 0.30 | 0.31 |  |  |  |  |  |
| 177952 | 0.295 | 0.31 |  |  |  |  |  |
| 177964 | 0.29 | 0.31 |  |  |  |  |  |
| 177973 | 0.285 | 0.31 |  |  |  |  |  |
| 177984 | 0.279 | 0.31 |  |  |  |  |  |
| 177995 | 0.275 | 0.31 |  |  |  |  |  |
| 178009 | 0.30 | 0.31 |  |  |  |  |  |
| 178013 | 0.313 | 0.31 |  |  |  |  |  |
| 178034 | 0.32 | 0.31 |  |  |  |  |  |
| 178043 | 0.325 | 0.31 |  |  |  |  |  |
| 178075 | 0.303 | 0.31 |  |  |  |  |  |
| No BBLR1 |  | Vertical rms orbit |  |  |  |  |
|  | 0.2985 | 0.311 |  |  |  |  |  |
| BBLR1 @ 122.5A |  |  |  |  |  |  |
| 178120 | 0.3013 | 0.3013 | 0.717 |  |  |  |  |
| BBLR1 and 2 @ 122.5A |  |  |  |  |  |  |
| 178137 | 0.2984 | 0.3 | 0.16 |  |  |  |  |
| 178150 | Moving BBLR2 |  |  | steps |  |  |  |
| 178165 | 0.2983 | 0.3092 | 0.12 | 1 |  |  |  |
|  | 0.2974 | 0.3091 | 0.1 | 2 |  |  |  |
|  | 0.2964 | 0.3101 | 0.07 | 3 |  |  |  |
| 178176 | 0.2973 | 0.311 | 0.05 | 4 |  |  |  |
| 178179 | 0.2954 | 0.312 | 0.002 | 5 |  |  |  |
| 178183 | 0.295 | 0.31 |  | 4 | BBLR2 positions | Initial (out) | Final |
| 178188 | 0.295 | 0.31 |  |  |  | 1436 | 1030 |
| 178200 | 0.29 | 0.31 |  |  |  | 3120 | 2709 |
| 178211 | 0.286 | 0.31 |  |  |  |  |  |
| 178221 | 0.28 | 0.31 |  |  |  |  |  |
| 178230 | 0.275 | 0.31 |  |  |  |  |  |
| 178242 | 0.295 | 0.31 |  |  |  |  |  |
| 178247 | 0.3 | 0.31 |  |  |  |  |  |
| 178256 | 0.307 | 0.31 |  |  |  |  |  |
| 178267 | 0.311 | 0.31 |  |  | Half PS intensity |  |  |
| 178275 | 0.31 | 0.31 |  |  | Full PS intensity |  |  |
| 178287 | 0.31 | 0.31 |  |  |  |  |  |
| 178289 | 0.316 | 0.31 |  |  |  |  |  |
| 178297 | 0.322 | 0.31 |  |  |  |  |  |
| 178307 | 0.326 | 0.31 |  |  |  |  |  |
| 178319 | 0.295 | 0.31 |  |  |  |  |  |
| 178335 | Bump @ dump [mm] | Intensity |  |  |  |  |  |
|  | -7 | 5.00E+11 |  |  |  |  |  |
|  | Use of BCT4 |  |  |  |  |  |  |
| 178347 | Kick timing change | Initial | Final |  |  |  |  |
| 178381 | (observe diffusion | 3500 | 700 |  |  |  |  |
|  | with PMTs) |  |  |  |  |  |  |
| 178385 | 0.304 | 0.31 |  |  |  |  |  |
| 178395 | 0.304 | 0.31 |  |  |  |  |  |
| BBLR1 @ 122.5A |  |  |  |  |  |  |
| 178408 | 0.303 | 0.311 |  |  |  |  |  |
| 178420 | 0.303 | 0.311 |  |  |  |  |  |
| 178423 | 0.303 | 0.311 | only H kick (6mm) |  |  |  |  |
| 178431 | 0.303 | 0.311 |  |  |  |  |  |
| 178434 | 0.303 | 0.311 | only V kick (6mm) |  |  |  |  |
| 178442 | 0.303 | 0.311 |  |  |  |  |  |
| 178445 | 0.303 | 0.311 | Both planes (6mm) |  |  |  |  |
| NO BBLR |  |  |  |  |  |  |
| 178450 | 0.301 | 0.31 |  |  |  |  |  |
| 178452 | 0.304 | 0.31 |  |  |  |  |  |
| 178464 |  |  | Problem with fixed |  |  |  |  |
|  |  |  | target beam probably |  |  |  |  |
|  |  |  | no influence in P2 |  |  |  |  |
| 178475 | THE END |  |  |  |  |  |  |