09.11.04 BBLR MD crossing scheme

19:40 TOTEM beam 4 bunches

intensity  2.1-2.2e11

exN~1.3

We see noise <0.1%  on BCT4

20:00  c.o. rms 1.7/1.3 mm

BBLR51760 -1.38 mm

0.31/0.30

decoupling -> no signal in other plane

eyN=1.5

on Timing BBLR -500 -> 0

off Dump -> beginning

kick 3450

H+V

4 mm ~5%losses

20:20 logging BCT has been ON

20:40 launching logging BICMON

20:30 BBLR1 ON +270 A

20:45 beam @ about 10 mm Delta QH =-0.012, DeltaQV=+0.016

beam losses due to third integer

change the tunes toavoid the resonance

new starting point

beam position at 0 mm,

wire ON QV=0.2798, QH=0.3022

now bump Delta y +12.3 mm

QH=0.2826, QV=0.3060

Delta QV=0.0262 , Delta QH=-0.0196 (going from center to bump position with BBLR on)

Vertical change is close to expectation

Horizontal change is further off

We explore if beam is centered horizontally

Move +2 mm in x (1.99)

QH=0.2817, QV=0.3059

-2 mm beam loss?! Reason unknown

-1.2 mm 21:12:00 sc 36847

QH=0.2819, QV=0.3060, large losses

-1.2 mm 120 A BBLR1

now on the coupling resonance 21:22 sc 36844

center beam with respect to BBLR1

moved tune QV to initial value

bump +10.2 mm

initial QH=0.3083, QV=0.3012, 0 A

final QV=0.0.3112, QH=0.2991, 120 A

0 H no coupling

-2 mm H coupling back 55/200 (second peak/main peak)

-1 mm 26/200

0 no coupling

1 no coupling (<10/200)

2 mm 20/165

3 mm 39/124=63/200

21:50 center @ 0.5 mm H for BBLR1

now check vertical separation for Iw=135 A

+10.5 mm V

QH=.3081, QV=0.3012 BBLR off

0.2975, 0.3128 BBLR on at 135 A

-0.0106, 0.0116 Delta Q

0.0137,0.0146 expected

+11.4 mm

0.2956, 0.3158

0.0125,0.0146

A beam at 11.4 mm V (BPM) is at 10 mm for BBLR1

22:15

-18.3 mm horizontal sc 37074

(-18.2 mm should be below 45 degree wire)

off

QH =0.3080, QV=0.3011

On, 135 A

QH=0.3259, QV=0.2875, some coupling (30/102)

DeltaQH=0.0179, DeltaQV=-0.0136

(expected 0.0169, -0.0127)

bump 0.7 mm

22:22 sc 37099

about 0.1% change in both planes as expected

A beam at -17.6 mm H (w.r.t to +0.5 mm center BBLR1 above)

is at the correct position underneath BBLR2

------------------------------------------------------------

We go to the center position between BBLR1 and BBLR2

+8.7 mm

22:43 sc 37171

22:44:49 135 A BBLR1

coupling becomes worse

we invert the polarity of BBLR1 09.11.04 22:47 sc 37206

coupling disappeared

tunes .3083, .3012 BBLR at 135 A

remember kick is at 3450

orbit corrected 23:01 37237

now at target position, zero coupling

QH=..3102 QV=2992, both BBLRs at 135 A

Switch off BBLRs

Both on at 95 A

QH=0.3100,QV=0.2983

Both off sc ~37256

QH= 0.3080 ,QV=0.3012

Change -0.002, 0.002

Expected -0.001, 0.001

QH=0.3264 sc 37279 lifetime improved

QV=0.2995

QH=0.322?

lifetime ~1000 s stable

move QH by small step to study sensitivity at this tune

sc 37328 QH=0.3167, QV=3002, lifetime ~500 s

sc 37342 QH=0.3278, QV=0.2992, lifetime ~500 s

sc 37368 QH=0.3177 , QV=0.3003

sc 32376 QH=0.3216,QV=0.3003

now scan y tune, both BBLRs off

sc 37389 QH=0.3217 ,QV=0.3052

sc 37395 QH=0.3210,QV=0.3111

sc 37400 QH=0.3218, QV=0.3158

sc 37405 QH=.3218,QV=0.3217

sc 37411, QV=0.3257

sc 37415, QV=0.3297

sc 37432, QV=0.3011 initial value

sc 37436, QV=0.2954

sc 37440, QV=0.2896

sc 37446, QV=0.2848

sc 37451, QV=0.2797

sc 37458, QV=0.2757

sc 37464, QV=0.2690

sc 37470, QV=0.3002

cannot take 1000 turn data due to computer network problem

took wire scans

sc 37527 QH=0.3219,QV=0.3012

now switch both BBLRs on at 95 A

sc 37529 QH=0.3230,QV=0.2994

wire scans

kick 2 mm

increase kick further

kick 4 mm

sc 37557

kick 5 mm

sc 37564

now scan y tune both BBLRs on at 95 A

sc 37570 QV=0.3042

sc 37577 QV=0.3090 00:37, lifetime 90 s

sc 37582, QV=0.3138

sc 37586, QV=0.3186

sc 35592, QV=0.3237

sc 35598, QV=0.3284

sc 37604, QV=0.2943

sc 37610, QV=0.2876

sc 37616, QV=0.2827

sc 37622, QV=0.2779

sc 37628, QV=0.2739

sc 37634, QV=0.2682

wire scans

back at nominal

sc 37672

1:03 190 A BBLR1, BBLR2 off

coupling correction

sc 37703 coupling knob 0.018 100/500 ~20%

0.016 120/400 (higher)

0.022

0.019  100/500

(0.004 standard)

0.02 best

closed orbit corrected

start y wire tune scan only BBLR1 on at 190A

sc 37725 QH=0.3227, QV=0.3002

sc 37739 QV=0.3043

sc 37745 QV=0.3106

sc 37752 QV=0.3145

sc 37757 QV=0.3184

sc 37762 QV=0.325 (or 0.324)

sc 37771 QV=0.3003 (back at original tunes)

wire scans

sc 37783 QV=0.2954

sc 37789, QV=0.2913

sc 37794, QV=0.2845

sc 37798, QV=0.2797

sc 37803, QV=0.2750

sc 37808, QV=0.2700

sc 37814, QV= 0.2993 (back to original)

01:49 move back horizontally to be under BBLR1 and down by 2.9 mm

so that the total distance is 12.9 mm

01:52 tune back at original reference

sc 37848

8.7 mm from beam axis

21.4-8.7 =12.7

tune shift should be 0.012 H  and 0.012 V

BBLR1 off sc 37891 QH=0.3101,QV=0.3112 OK (0.012 in V)

wire scans?

start y wire tune scan only BBLR1 on at 190A with beam 12.7 mm below BBLR1

sc37914 QH=0.3216, QV=0.3041

sc37919, QV=0.3110

sc37924, QV=0.3184

sc37930, QV=0.3238

sc37935, QV=0.2992

sc37940, QV=0.2935

sc37945,QV=0.2895

sc37950, QV=0.2847

sc37955,QV=0.2798

sc37960, QV=0.2759

sc37965,QV=0.2701

wire scans

02:32

scan of beam-wire distance (onset of strong diffusion)

QH=0.3208, AV=0.2914

sc37998, + 1 mm closer towards the wire

sc38004 last point

correct tunes at each point

sc38009 +2 mm closer towards the wire

sc38014 end point

sc38018 +3 mm QH=0.3219, QV=0.2887

sc38024 end

sc38031 +4 mm

sc38035 end

sc38040 +5 mm

wire scans

sc38066 -2 mm, tunes corrected

sc38072  end

sc38076 -4 mm, tunes corrected

sc38089 end

sc38096 -1 mm, tunes corrected